## Slide 1
MICROPROCESSOR CSC 405
Subject Incharge
Dakshata Panchal
Assistant Professor
email: dakshatapanchal@sfit.ac.in
St. Francis Institute of Technology
Department of Computer Engineering
1
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 2
CSC405 Microprocessor Module 2
Instruction Set and Programming
2
St. Francis Institute of Technology
Department of Computer Engineering
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 3: Contents as per syllabus
Addressing Modes
Instruction set – Data Transfer Instructions, String Instructions, Logical Instructions, Arithmetic Instructions, Transfer of Control Instructions, Processor Control Instructions
Assembler Directives and Assembly Language Programming, Macros, Procedures
Mixed Language Programming with C Language and Assembly Language.
Programming based on DOS and BIOS Interrupts (INT 21H, INT 10H)
3
St. Francis Institute of Technology
Department of Computer Engineering
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 4
The different ways in which a processor can access the operands of an instruction are called Addressing Modes.
Operands can be located anywhere
  Memory locations
  Registers
  I/O ports
  Present in the instruction itself.
4
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 5
A command given by the user to perform a certain task
It is written in a specific format
Opcode Operand field(s)
Opcode is a unique hexadecimal encoding of the given instruction.
Opcode depends on the operation as well as the operand fields.
5
St. Francis Institute of Technology
Department of Computer Engineering
Instruction
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 6
Generally all instructions have
Operation (mnemonic)
Destination (operand)
Source (operand)
Mnemonic Destination, Source
Some instructions may have only destination, while some may have more than one source, or more than one destination. (details later)
6
St. Francis Institute of Technology
Department of Computer Engineering
Instruction
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 7
Source of data can be:
  Immediate data (available on the instruction)
  A register
  Specified address (memory or I/O)
Destination can be:
  A register
  Specified address (memory or I/O)
7
St. Francis Institute of Technology
Department of Computer Engineering
Instruction
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 8
There are 5 fundamental addressing modes
Immediate addressing Mode
Register Addressing Mode
Direct Addressing Mode
Indirect Addressing Mode
  Register Indirect
  Register Relative
  Base Index
  Base Relative Indexed
Implied Addressing Mode
8
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 9
9
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
1. Immediate addressing Mode:
In this mode, data is given in the instruction
Doesn’t involve computation of address
Example:
  MOV AX, 0170h
AX
0000 0001 0111 0000
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 10
2. Register Addressing:
10
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
In this mode, Data is given by the Register.
The operands on which instruction operate are stored in the specified registers
For 16-bit operand – AX, BX, CX, DX, SI, DI, SP, BP
For 8-bit operand – AH,AL, BH,BL, CH,CL, DH,DL
Example:
MOV AX, BX
1234
1234
BX
AX
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 11
3. Direct Addressing:
11
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
In this mode, Address is given in the instruction
Example: MOV AX, [1050H]
(or) MOV AX, DATA
By default DS is segment address
let, DS = 2000h
EA = 2000*10 + 1050 = 21050
Back
34
1234
21050
AX
12
21051
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 12
Practice:
12
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
  Assume with in data segment,
  Take the data of location 4000 into BL
  Take the data of location 5000 into CL
  Add Both BL and CL, so that results comes in BL
  Then add number “40” into BL and results in BL
  Finally store the result in location 6000
  Write the instruction?
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 13
Practice:
13
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
  Answer:
  MOV BL,[4000]
  MOV CL,[5000]
  ADD BL,CL
  ADD BL,40
  MOV [6000], BL
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 14
4. Indirect Addressing:
In this mode, Address is given in Register
Types of Indirect Addressing Mode:-
  Register Indirect Addressing
  Register Relative Addressing
  Base Index Addressing
  Base Relative Indexed Addressing
14
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 15
4(a): Register Indirect Addressing:
15
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Address given by the Register
Address of the data is present in one of the base or index registers – BX, BP, SI or DI
Offset is always 16-bits wide
Data can be 8-bit or 16-bit
Example: MOV AL, [BX]
let BX = 1050 & DS = 2000
then EA = 2000*10 + 1050 = 21050
Back
12
12
21050
AL
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 16
4(a): Register Indirect Addressing:
Suppose in the data segment there is some location, let's say 6000 and we want any register(let’s say CL )to contain the data from that location.
How can we write the instruction??
Use direct addressing mode
Or
Indirect addressing mode
16
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 17
4(a): Register Indirect Addressing:
Using direct addressing mode
MOV CL,[6000]
CLDS :[6000]
Or
Indirect addressing mode
MOV BX, 6000
MOV CL,[BX]
CL,DS:[6000]
17
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
So What’s the difference??
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 18
To understand the difference 
Answer few Question?
Get the data from location 6000 which addressing mode will you use?
Ans: Direct addressing mode
MOV CL,[6000]
CLDS :[6000]
Now get the data of 100 locations starting from location 6000, so which addressing mode will you use?
18
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 19
Ans: if you use Direct addressing mode, then
100 times you need to write the same instruction
MOV CL,[6000]
MOV CL,[6001]
MOV CL,[6002]
MOV CL,[6003] …. And so on
Is it feasible????
No!!!
19
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 20
Ans:
But if we use indirect addressing mode, then MOV BX, 6000
MOV CL, [BX]
INC BX
CLDS:[6000]
20
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 21
Ans:
But if we use indirect addressing mode, then MOV BX, 6000
MOV CL, [BX] Put this in a loop
INC BX
CLDS:[6000]
So whenever we want to work on a series of location, we use indirect addressing mode.
21
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 22
Ques. Take the data from 2000 location to CL register and store it at location 3000. Which addressing mode will you use to write an instruction.
Ans:
Direct Addressing Mode
MOV CL, [2000]
MOV [3000], CL
22
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 23
Ques. Write a program to transfer a block of data from location 2000 to 3000
Ans:
MOV SI, 2000H
MOV DI, 3000H
MOV CL, [SI]
MOV [DI], CL
INC SI
INC DI
23
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 24
Ques. Block Inversion Program
Ans:
MOV SI, 2000H
MOV DI, 3000H
MOV CL, [SI]
MOV [DI], CL
INC SI
DEC DI
24
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 25
But we need to follow some Rule:
Rule 1:
In indirect addressing mode, address must
be given by specific Register.
There are 4 general purpose register, AX, BX, CX, DX.
Out of these only BX register can be used to give the memory address and Only these offset Register can be used BP,SI and DI
25
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 26
But we need to follow some Rule:
Rule 2:
If you use BX, SI or DI it will be used in data segment
If you use BP, by default it will work on stack segment
26
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 27
4(b): Register Relative Addressing:
27
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Effective Address is the sum of
  16-bit offset given in a base register (BX or BP)
  8 or 16-bit displacement (+ or – constant)
  Segment Register (DS or SS) * 10
Example: MOV AL, [BX+04]
let BX = 1050 & DS = 2000
then EA = 2000*10 + 1050 + 4 = 21054
Back
90
90
21054
AL
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 28
4(c): Base Indexed Addressing:
Index addressing:-
Used in arrays to access the nth element
Example: MOV AL, Array[3]
let Array = {10, 23, 08, 31}
if offset of Array = 1050 and DS = 2000
then EA = 2000*10 + 1050 + 3 = 21053
28
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
31
31
21053
AL
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 29
4(c): Base Indexed Addressing:
Effective Address is the sum of
16-bit offset given in a base register (BX or BP)
displacement in an index register (SI or DI)
Segment Register (DS or SS) * 10
Example: MOV AX, [BX+SI]
let BX = 1050 SI = 4 & DS = 2000
then EA = 2000*10 + 1050 + 4 = 21054
29
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
12
1234
21054
AX
34
21055
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 30
4(d): Relative Base Indexed Addressing:
Effective Address is the sum of 16-bit offset given in a base register (BX or BP)
+index register (SI or DI)
+8 or 16-bit displacement (+ or – constant)
+Segment Register (DS or SS) *10
Example: MOV AX, [BX+SI+20]
let BX = 1050 SI = 4 & DS = 2000
then EA = 2000*10 + 1050 + 4 + 20 = 21074
30
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
12
1234
21074
AX
34
21075
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 31
5. Implied/ Implicit Addressing:
No operands are used to execute these instructions
Example:
NOP : No Operation
CLC : Clear Carry Flag (CF = 0)
START: Execution Starts
31
St. Francis Institute of Technology
Department of Computer Engineering
Addressing Modes
Back
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 32
32
St. Francis Institute of Technology
Department of Computer Engineering
Instruction Set
Back
Processors execute a machine code.
MACHINE CODE: The sequence of numbers that flip the switches in the computer on and off to perform a certain job of work - such as addition of numbers, branching, multiplication, etc.
Machine specific and well documented by the implementers of the processor.
OPCODE: It is a number interpreted by your machine(virtual or silicon) that represents the operation to perform.
  E.g., MOV BX, data
  47H [1050] (47H is opcode for MOV into BX, 16-bits of memory)
CSC 405:Microprocessor
Ms. Dakshata P.

## Slide 33: Opcode & Operands
OPCODE is short for 'Operation Code'.
An opcode is a single instruction that can be executed by the CPU.
In machine language it is a binary or hexadecimal value such as 'B6' loaded into the instruction register.
In assembly language mnemonic form of an opcode is a command such as MOV or ADD or JMP
OPERAND is the data on which the operation is performed

## Slide 34: Instruction Format
General format of an assembly language instruction :
Label: Mnemonic Operand, Operand ;Comment
Every instruction starts on a new line
Labels must be followed by colon (:) (It is an identifier)
Instructions operate on implicit (zero), one, two, or three operands
Multiple operands must be separated by a comma
Comment is ignored by assembler

## Slide 35: 8086 Instruction Set
Instructions in 8086 are classified into the following 8 functional groups
  Data Transfer Instructions
  Arithmetic Instructions
  Bit Manipulation Instructions
  Branch Instructions
  String Operation Instructions
  Processor Control Instructions
  Iteration Control Instructions
  Interrupt Instructions

## Slide 36: 1. Data Transfer
MOV : R/M/D  R/M
XCHG : R/ M  R/M
LEA : EA of operand  R
PUSH/POP : Stack manipulation
PUSHA/POPA : Copy all registers  Stack
PUSHF/POPF : Flag register  Stack
IN/ OUT : R  port

## Slide 37: Data Transfer Instructions
Instruction | Syntax | Example
Move | MOV destination, source | MOV AX, BX
Exchange | XCHG destination, source | XCHG BL, AH
Load Effective Address | LEA reg16, source | LEA BX, AMOUNT
Push | PUSH source | PUSH DX
Pop | POP destination | POP AX
Push decrements SP by 2
PUSH DX : SP←SP-2; Contents of DX copied onto stack
Pop increments SP by 2
POP AX SP←SP+2; copy stack top contents to AX

## Slide 38: 2. Arithmetic and Logical Instructions
Add or Subtract (ADD / SUB)
Add/Subtract with Carry/Borrow (ADC / SBB)
Increment / Decrement (INC / DEC)
Compare / Negate (CMP / NEG)
ASCII adjust (AAA/ AAS/ AAM/ AAD)
Decimal Adjust (DAA/DAS)
Multiplication/Division (MUL/ IMUL/ DIV/ IDIV)
Logical (AND/ OR/ XOR/ NOT)
Convert (CBW/ CWD)

## Slide 39: Arithmetic Instructions
Instruction | Syntax | Example
Add / Subtract | ADD/SUB destination, source | ADD/SUB BX, AX
Add with Carry | ADC destination, source | ADC AH, 09H
Subtract with Borrow | SBB destination, source | SBB AH, 09H
Increment / decrement | INC/DEC destination | INC/DEC CL
Compare | CMP destination, source | CMP AH, BL
Negate | NEG destination | NEG BX
NEG: Negate changes sign of operand (2’s complement)
CMP: Compare
  If (dest > src) : CF=0, ZF=0, SF=0
  If (dest < src) : CF=1, ZF=0, SF=1
  If (dest = src) : CF=0, ZF=1; SF=0

## Slide 40: Arithmetic Instructions
Instruction | Syntax | Example
Multiply (unsigned) | MUL source | MUL BX
Divide (unsigned) | DIV source | DIV CX
Integer Multiply (signed) | IMUL source | IMUL CL
Integer Divide (signed) | IDIV source | IDIV CL
Accumulator is default operand in multiply and divide
MUL BX → DX:AX = AX*BX
MUL BH → AX = AL*BH
DIV BX → AX = Quotient; DX = Remainder
DIV BL → AL = Quotient; AH = Remainder

## Slide 41: Arithmetic Instructions
Instruction | Syntax | Example | 
 |  | Before | After
ASCII adjust for Addition | AAA | AH=00H, AL=0BH | AH=01H, AL=01H
ASCII adjust for Subtraction | AAS | AH=02H, AL=0BH | AH=01H, AL=05H
ASCII adjust for Multiplication | AAM | AH=00H, AL=30H | AH=04H, AL=08H
ASCII adjust for Division | AAD | AH=03H, AL=09H | AH=00H, AL=39H
Decimal adjust for Addition | DAA | AL=6BH | AL=71H
Decimal adjust for Subtraction | DAS | AL=2EH | AL=28H
AAA and AAS check only lower nibble of AL. DAA and DAS check lower and higher nibble of AL.
AAM : AL = AL/10, AH = AL mod 10
AAD : AL = AH*10+AL, AH=00H

## Slide 42: 3. Bit manipulation Instructions
Instruction | Syntax | Example
Logical AND | AND destination, source | AND AX, F000H
Logical OR | OR destination, source | OR BX, AX
Logical Exclusive OR | XOR destination, source | XOR AH, CH
Logical NOT | NOT destination | NOT AL
NOT inverts each bit in destination (1’s complement)

## Slide 43: Bit manipulation
Instruction | Syntax | Example | 
 |  | Before | After
Convert Byte to Word | CBW | AH=??, AL=10011011 | AH=11111111, AL=10011011
Convert Word to D Word | CWD | DX=?? AX=10101101 10010001 | DX=11111111 11111111 AX=10101101 10010001

## Slide 44: Bit manipulation
Instruction | Syntax | Example
Shift Logical Left | SHL destination, source | SHL BL, 1
Shift Logical Right | SHR destination, source | SHR BL, 1
Shift Arithmetic Left | SAL destination, count | SAL AL, 2
Shift Arithmetic Right | SAR destination, count | SAR AL, 2
Rotate Left/Right | ROL/ROR destination, count | ROL/ROR AX, 2
Rotate through carry Left | RCL destination, count | RCL CL, 4
Rotate through carry Right | RCR destination, count | RCR CL, 4
SAL is same as SHL, LSB becomes 0
In SHR, MSB is padded with 0. In SAR, MSB is padded with previous MSB bit

## Slide 45: 4. Branch Instructions
CALL : Call a subroutine
RET : Return to main procedure
JMP : Provide an address of the next instruction
  Unconditional Jump (JMP)
    Always jumps to specified address
  Conditional Jump (JZ, JNC...)
    Checks the status of certain flag bits (depending on the condition) and jumps only if condition is satisfied.

## Slide 46: 5. String Operation Instructions
Load
  string/ string byte/ string word (LODS/LODSB/LODSW)
Store
  string/ string byte/ string word (STOS/STOSB/STOSW)
Compare
  string/ string byte/ string word (CMPS/CMPSB/CMPSW)

## Slide 47: 6. Processor Control Instructions
STC : Set CF = 1
CLC : Clear CF = 0
CMC : Complement CF
STD : Set DF = 1
CLD : Clear DF = 0
STI : Set IF = 1
CLI : Clear IF = 0

## Slide 48: 7. iteration Control Instructions
LOOP: Jump back to address until CX = 0
LOOPE/ LOOPZ: Jump back to address until ZF = 1 and CF = 0
LOOPNE/ LOOPNZ: Jump back to address until ZF = 0 and CX = 0
JCXZ : Jump to address if CX = 0

## Slide 49: 8. Interrupt Instructions
INT : Interrupt execution by calling a stored program
INTO : Execute interrupt program if
OF = 1
IRET : Return from Interrupt to main program

## Slide 50: III. Assembly Language Programming

## Slide 51: Declaring Variables
Define Byte – DB
  SUM DB 0
Define Word – DW
Define Double Word – DD
Define Quad Word – DQ
Define Ten Bytes – DT
Arrays – DUP(size)
  LIST DB DUP(20)

## Slide 52: Program Directives
SEGMENT
ENDS
ASSUME
OFFSET
END
PROC
ENDP

## Slide 53: DOS System Call: INT 21H
Chararcter I/O
File Operations
Record Operations
Directory Operations
Disk Management
Process Management
Memory Management
Network Functions
Time and Date Functions
Miscellaneous System Functions
Reserved Functions

## Slide 54: IV. Mixed Language Programming

## Slide 55: Mixed Language Program
Can be used with C/C++
Called inline assembler. Used to insert short, limited assembly language code
Need to use an asm block inside main function
No need to use data definition directives

## Slide 56: Assembly Program
    data segment
    ..........
    data ends
    code segment
    assume cs:code,ds:data
    start:
    mov ax,data
    mov ds,ax
    /*
    instructions
    */
    code ends
    end start

## Slide 57: C/C++ program
    void main()
    {
    int a,b;
    int c=0;
    clrscr();
    printf("Enter 1st no : ");
    scanf("%d",&a);
    printf("Enter 2nd no : ");
    scanf("%d",&b);
    c = a + b;
    printf("Sum = %d",c);
    getch();
    }

## Slide 58: Example
    void main()
    {
    int a,b;
    int c=0;
    clrscr();
    printf("Enter 1st no : ");
    scanf("%d",&a);
    printf("Enter 2nd no : ");
    scanf("%d",&b);
    asm{
      mov ax,a
      mov bx,b
      add ax,bx
      mov c,ax
    }
    printf("Sum = %d",c);
    getch();
    }

## Slide 59: Assembly program - Examples
Addition of 2 nos

## Slide 60: Assembly Programming
STEP 1: Define variables (numbers, strings, arrays, etc.)
data segment
msg1 db 10,13, “Enter 1st no : ”
msg2 db 10,13, “Enter 2nd no : ”
msgres db 10,13, “result : ”
data ends

## Slide 61: Assembly Programming
STEP 2: Define code segment, move data into ds
code segment
assume cs:code, ds:data
start:
mov ax,data
mov ds,ax

## Slide 62: Assembly Programming
STEP 3: Take input
mov ax,data
mov ds,ax
; display msg1
mov dx,offset msg1
mov ah,09h
int 21h
; Take 1st no input
mov ah,01h
int 21h
;convert ascii to decimal
sub al,30h
mov bl,al
; repeat for 2nd no

## Slide 63: Assembly Programming
STEP 4: add and store
mov ah, 00h
add al, bl
aaa
mov cx,ax
; convert decimal to ascii
add cx,3030h

## Slide 64: Assembly Programming
STEP 5: display result
mov ah, 09h
mov dx, offset msgres
int 21h
mov dl,ch
mov ah,02h
int 21h
mov dl,cl
mov ah,02h
int 21h

## Slide 65: Assembly Programming
STEP 6: Terminate program
mov ah, 4ch
mov al, 00h
int 21h
code ends
end start

## Slide 66: Questions

## Slide 67
THE END!
Have a nice day!